## Slide 1: ENERGY RESOURCES

## Slide 2: What is energy?
The ability to do work.
Comes in different forms: Heat(thermal), Light(radiant) and Motion(kinetic)

## Slide 3: ENERGY SOURCES

## Slide 4: 1. RENEWABLE ENERGY

## Slide 5
SOLAR
WIND
HYDROELECTRIC
BIOMASS
GEOTHERMAL

## Slide 6: 2. NON-RENEWABLE ENERGY

## Slide 7
COAL
OIL
NATURAL GAS
NUCLEAR

## Slide 8: COAL
A combustible black or brownish-black sedimentary rock usually occurring in rock strata in layers or veins called coal beds or coal seams.
Anthracite= hard form of coal: regarded as metamorphic rock.
Composed primarily of carbon along with variable quantities of other elements (H,S,O, and N)

## Slide 9: What is petroleum (oil and gas) and how is it formed?
Under these conditions, the nitrogen, sulfur and phosphorus atoms is converted into kerogen (an intermediate material made up of H2O, CO2 and H) Which is then transformed into oil or gas.
    @2000m below, with 100 °C, kerogen starts to release hydrocarbons.
    Between 2000 and 3800m (AKA the oil window) kerogen turns into oil.
    In between 3800 and 5000m, the production of liquid hydrocarbons peaks(AKA Gas Window).
    The proportion of liquids and gas generated depends on the type of source rock. (If the organic debris are from animal origin, it will produce more oil than gas. (VV).

## Slide 10: GEOTHERMAL ENERGY
As we descend deeper into the Earth’s crust, underground rock and water become hotter.
This heat can be recovered using different geothermal technologies depending on the temperature .
The heat resources are not inexhaustible.

## Slide 11: Different types:
Low-temperature geothermal energy
At 20 degree Celsius to 90 degree Celsius ,the heat and water are used for geothermal heating.
Medium-temperature geothermal energy
At 90 degree Celsius to 160 degree Celsius, the water is used on the surface in liquid form.
High-temperature geothermal energy
At temperatures above 160 degree Celsius, the water turns into steam when it reaches the Earth’s surface.
Drive turbines to generate power.

## Slide 12: Hydropower, the leading renewable energy
Widely used for decades, hydropower plants are the world’s leading renewable energy source, producing 83% of renewable energy.
The kinetic energy generated by moving water drives watermills to produce mechanical energy.
Modern hydropower, sometimes referred to as “white coal”, is harnessed in plants where electricity is generated.

## Slide 13: TYPE OF HYDROPOWER PLANT
“SMALL HYDRO”
Uses the flow of the river or dams less than 25 meters high.
OFF-STEAM PLANTS
Are modular (energy can be produced on demand) with dams (about 20-300 meters high) that can release water as required.
PUMPED STORAGE POWER PLANTS
Modular, with two reservoirs at different heights.
DEPENDS ON THE SIZE OF DAMS/WATER RESERVOIS

## Slide 14: ADVANTAGES OF HYDROPOWER
Renewable and storable.
Operating and maintenance costs are low.
Extremely efficient
    About 90% of the water’s energy is converted into electricity.